Buzzer

The digital clock buzzer shall be a Sapling Buzzer. It shall be activated by the relays on any of Sapling’s 3300 digital clock models. It shall operate on voltages between 4.0 and 7.0 VDC. Without the wires, it shall be 12mm in diameter and 10mm in height. It shall produce a decibel level of 85 db/min (measured in an open-air environment).

| The Sapling Company, Inc. | Tel. +1.215.322.6063 |
| --- | --- |
| 670 Louis Drive | Fax. +1.215.322.8498 |
| Warminster, PA 18974 | www.sapling-inc.com |
| U.S.A. |  |