Network Repeater

The repeater shall be a Sapling Network Repeater. It shall receive time data via TCP/IP from any Sapling 2000 or 3000 Master Clock. The repeater shall transmit data on a frequency of either 915-928 MHz or 2.4 GHz, depending on the hardware that was ordered. This will allow it to communicate with wireless SAL(G*) Analog and SBL(G**) Digital clocks operating on the same frequency range using frequency-hopping technology. The repeater shall have a maximum antenna size of seven (7) inches, an RF input sensitivity of –103dbm, a power output of 27 dBm, and shall be FCC approved. The voltage input for the repeater shall be 115V/60Hz or 230V/50Hz.

* (G) is used for 2.4GHz models, in which case the model code is SALG. In 900MHz models, the model name is SAL.

** (G) is used for 2.4GHz models, in which case the model code is SBLG. In 900MHz models, the model name is SBL.

| The Sapling Company, Inc. | Tel. +1.215.322.6063 |
| --- | --- |
| 1633 Republic Road | Fax. +1.215.322.8498 |
| Huntingdon Valley, PA 19006 | www.sapling-inc.com |
| U.S.A. |  |