SAI Series Analog Clock

The quartz analog clock shall be a Sapling SAI Series analog clock and will be used as a stand–alone analog clock. The clock will have a low–profile, semi–flush smooth surface metal case. The crystal will be a shatterproof, side molded polycarbonate material. Glass and visible molding marks are unacceptable. The clock shall have a white dial with black numerals. Dials are to be made of durable polystyrene materials. The clock is to have black hour and minute hands, as well as a red second hand. The movement is to be a quartz movement with an accuracy of ± 0.8 sec./day @ 1.5 volts. The clock shall have a battery life of approximately one (1) year. The quartz movement is to operate at a frequency of 32.768 KHz. The Sapling SAI Series analog clock shall operate on a single “AA” battery.