SBL 1000 Series Digital Clock

The clock shall be a Sapling SBL 1000 wireless digital clock and shall have either a full 2.5” or 4.0” high efficiency red LED numeral display. The clock shall be available in both four (4) and six (6) digits.  The clock will operate as a wireless digital slave clock. The clock shall receive signals from other clocks in the surrounding area or from the transceiver. The clock shall receive and transmit with 915–928MHz frequency–hopping technology. The clocks will be capable of transmitting and receiving the time without interfering with each other. The clock shall have data LEDs on the board to display the receiving of data. It shall have a 12 or 24 hour display format. The clock will have two (2) levels of adjustable brightness and will feature immediate correction for time changes. The digital clock shall be capable of being installed either surface or double mount.  When the input is lost, the colon on the display of the clock shall flash. The clock shall have an anti–glare red filter with a smooth surface. No external screws shall be visible on the bezel or clock housing. The clock shall be FCC compliant, part 15 Section 15,247.